# Variables
A variable stores data that can be changed later on. Project with Flow support can have both global and local variables. Global variables are visible from all Flows, local variables are visible only inside the Flow in which it is defined.

Project without Flow support can have only global variables and those variables must be Native i.e. variables managed by the native code (written in C++).

To add variables, use the Variables panel (Fig. 1), when a dialog box will open for defining the basic parameters of the variable (Name, Type and Default value).

To edit the parameters of the variable selected in the Variables panel, use the Properties panel. In Fig. 2, Fig. 3 and Fig. 4 shows Properties panels for different types of variables from different types of projects.

Fig. 1: Variables panel	Fig. 2: Variable Properties panel (EEZ-GUI)

Fig. 3: Variable Properties panel (LVGL)	Fig. 4: Variable Properties panel (Dashboard)

Item	Description
Id	ID is EEZ-GUI project specific and is used in Page, Action, Global Variable, Style, Font, Bitmap and Colors. These are all resources that are referenced by name in the project editor. When that project is built, names are no longer used, but numerical IDs. This field is optional, i.e. an ID does not have to be specified, in which case an ID will be assigned during the build. However, if we want an object to always get the same ID, then it needs to be defined. Why would we want to always have the same ID? This is necessary when there is a master project such as modular-psu-firmware.eez-project from EEZ BB3 and that master project is used by BB3 Applets and BB3 MicroPython scripts and they can use resources from the master project that have that ID defined. / Important: once the ID is set, it should not be changed, otherwise all BB3 scripts that depend on it should be rebuilt.
Name	Variable is referenced in other parts of project by its name. / Rules for naming variables: Starts with a letter or an underscore (_), followed by zero or more letters, digits, or underscores. Spaces are not allowed.
Description	Optional field, contains a description of the variable.
Type	The type of data stored in variable. When adding a new variable, its suggested default value will depend on the selected type (0 for Integer, False for Boolean, etc.).
Native	The variable is managed by the native code (written in C++). / A Dashboard project cannot have Native variables, and working with them is explained in Chapter XX.
Default value	Default value is the initial value of the variable when Flow starts. Given in JSON notation (https://www.json.org/json-en.html). / For example: 123, "Hello", true / If types is struct: { "member1": 42, "member2": "Hello" } / If type is array: [1, 2, 3] or ["string1", "string2", "string3"]
Default value list	Only supported in EEZ-GUI project that does not have EEZ Flow enabled.
Used in	See Configurations in project Settings.
Persistent (Global variables only)	Stores the last value of the variable in the .eez-runtime-settings file, so that next time projects will have this value, instead of the default value. / Supported only in Dashboard projects.

## Variables usage
Variables are used in the project with EEZ Flow enabled. Data stored in a variable can be accessed using expressions. The following Action components are used to work with variables:
- Evaluate – evaluates expression, which can use variables, and sends the result through "result" data line.
- Watch – monitors the change in the value of the variable. At Flow start, it always sends the current value via the Changed data flow line, and later every value change is sent.
- SetVariable – sets a new variable value. Multiple entries are allowed. Each entry contains a variable and an expression field. During Flow execution, the evaluated expression will be stored in a variable.
- SwitchCase, Compare, IsTrue – Actions used for branching in the Flow depending on the value of the variable
Variables are also used in Widget components. Certain Widget properties can be defined as an expression. In this case, the value of that property will change during Flow execution as the expression changes. For example, Label widget can show the content of some variable, and it will updated every time this variable has been modified.

## Variable types
### Basic/Primitive types
Item	Description
Integer	Signed 32-bit integer.
Float	IEEE 4-byte floating-point.
Double	IEEE 8-byte floating-point.
Boolean	Can hold true of false value.
String	Sequence of characters.
Date	Unix timestamp.
Blob	Binary large object (Dashboard projects only).
Stream	Stream of data (Dashboard projects only).
Any	Can hold any data type.

### Structures
Structure types are defined in Variables panel in Structs section. Struct type variable stores multiple data values each accessed by its member name. Each member is defined by its name and type.

Structures can only be used in projects that have EEZ Flow enabled.
### Enums
Enums types are defined in Variables panel in Enums section. Enum type variable stores integer data value, but can contain only restricted set of values. Each enum member is defined by its name and integer value.
### Objects
Object variables, similar to structs, can hold multiple values, each accessed by member names. The member names depends of the type of Object variable. Example of object variables: Instrument connection or PostgreSQL connection. Object variables are described in more detail in Chapter XX.

Object variables can only be used in Dashboard projects.
### Arrays
Array variable stores multiple data values.
### Expressions
An expression contains instructions on how to evaluate a data value during Flow execution. An expression is defined in code similar to JavaScript or other C-like languages.

Expression element	Description / Example
Literal value	Example: 42, "Hello", true
Variable names	Example: my_var
Input names	Retrieves the data stored in data input using the name of that input. / Example: input_name
Binary operator	Example: my_integer_var + 1
Logical operator	Example: my_integer_var < 10
Unary operator	Example: -my_integer_var
Ternary operator	Example: my_integer_var == 1 ? true : false / (evaluates to True if my_integer_var is 1, otherwise evaluates to False)
Function calls	Example: String.length(my_string_var)
Parentheses “()”	Specifying the order of the evaluation / Example: "Counter: " + (a + 1)
Accessor “.”	Structure type member accessor by using “.” / Example: my_struct_var.member1
Accessor “[]”	Array element accessor by using “[]” / Example: my_array_var[3], my_array_var[index]
Enum value	Example: MyEnumTypeName.Member1

Expression examples:

`var[i].member1`
	`var` is array which contains structs, which has member `member1`
	`i` is integer variable
	evaluates to `member1` value in the i-th element

`var == State.START || var == State.EMPTY`
	var is of type enum:State, and State enum has two members: START and EMPTY
	evaluates to True if var contains data that is either State.START or State.EMPTY

### Literals
Type	Description / Example
Integer	`42`
Float or double	`3.14`
String	`"Hello world!"`
Translated string	T"text_resource_id" (prefix T is mandatory)
Boolean	`true` or `false`
JSON	See https://www.json.org/json-en.html

### Binary Operators
Each binary operators requires two arguments. Binary operator is written between arguments, for example: <arg1> + <arg2>

+ Addition

Rules:
- If any of the arguments is a string then result is a string. For example, `voltage +" V"` will evaluate to `"1.5 V"` if data stored in voltage variable is `1.5`
- If any of the arguments is a double then result is a double.
- If one argument is a float and the other is a float or an integer the result will be a float.
- If both arguments are integers then result is an integer.

arg1\arg2	integer	float	double	string	boolean	other_type
integer	integer	float	double	string	integer	err
double	double	double	double	string	double	err
float	float	float	double	string	float	err
string	string	string	string	string	string	err
boolean	integer	float	double	string	integer	err
other_type	err	err	err	err	err	err

Subtraction -

arg1\arg2	integer	float	double	boolean	other_type
integer	integer	float	double	integer	err
double	double	double	double	double	err
float	float	float	double	float	err
boolean	integer	float	double	integer	err
other_type	err	err	err	err	err

Multiplication *

arg1\arg2	integer	float	double	boolean	other_type
integer	integer	float	double	integer	err
double	double	double	double	double	err
float	float	float	double	float	err
boolean	integer	float	double	integer	err
other_type	err	err	err	err	err

Division /

arg1\arg2	integer	float	double	boolean	other_type
integer	integer	float	double	integer	err
double	double	double	double	double	err
float	float	float	double	float	err
boolean	double	float	double	double	err
other_type	err	err	err	err	err

Remainder %

arg1\arg2	integer	float	double	boolean	other_type
integer	integer	float	double	integer	err
double	double	double	double	double	err
float	float	float	double	float	err
boolean	integer	float	double	integer	err
other_type	err	err	err	err	err

Left shift <<

arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

Right shift >>

arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

Binary AND &

arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

Binary OR |

arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

Binary XOR ^

arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

### Logical operators
Logical operators are also binary operators that result in Boolean values.

Type	Description
==
!=
<
>
<=
>=
&&
||

### Unary operators
Type	Description
+
-
~
!

### Conditional (ternary) operator
The conditional (ternary) operator is the only operator that takes three operands: a condition followed by a question mark (?), an expression to be executed if the condition is true followed by a colon (:), and finally an expression to be executed if the condition is false.
## Functions
### System
System.getTick
Description:	Retrieves the number of milliseconds that have elapsed since the flow execution was started.
Parameters:	None
Return value:	Type: Integer
	Description: Value in milliseconds.

### Flow
Flow.index
Description:	Index of current element in the List and Grid widget. Check the description of these two widget for the more information.
Parameters:	Name: index
	Type: Integer
	Description: ???
Return value:	Type: Integer
	Description: Element index.

Flow.isPageActive
Description:	If this function is executed inside the page it will return true if that page is currently active page, otherwise it will return false.
Parameters:	None
Return value:	Type: Boolean
	Description: True if page is active, False if page is not active.

Flow.pageTimelinePosition
Description:	If this function is executed inside the page or custom widget it will return the current position at the animation timeline for that page or custom widget.
Parameters:	None
Return value:	Type: Boolean
	Description: Timeline position.

Flow.makeValue
Description:	Creates a new value of type Struct.
Parameters:	Name: structName	Type: String	Description: Structure name.
	Name: value	Type: JSON	Description: Structure value.
Return value:	Type: Struct
	Description: Created struct value.

Flow.makeArrayValue
Description:	Creates a new value of type array.
Parameters:	Name: value
	Type: JSON
	Description: Array value.
Return value:	Type: Array
	Description: Created array value.

Flow.languages
Description:	Retrieves a list of languages defined in multi-language project as array of strings.
Parameters:	None
Return value:	Type: Array:string
	Description: Array of languages.

Flow.translate
Description:	Translate text resource ID, same as T"textResourceID".
Parameters:	Name: textResourceID
	Type: String
	Description: Text resource ID.
Return value:	Type: String
	Description: Translated string.

Flow.parseInteger
Description:	Parse integer value given as string.
Parameters:	Name: str
	Type: String
	Description: Input string.
Return value:	Type: Integer
	Description: Parsed integer value.

Flow.parseFloat
Description:	Parse float value given as string.
Parameters:	Name: str
	Type: String
	Description: Input string.
Return value:	Type: Float
	Description: Parsed float value.

Flow.parseDouble
Description:	Parse double value give as string.
Parameters:	Name: str
	Type: String
	Description: Input string.
Return value:	Type: Double
	Description: Parsed double value.

### Date
Date.now
Description:	Returns current date.
Parameters:	None
Return value:	Type: Now
	Description: Current datetime.

Date.toString
Description:	Converts given date to string.
Parameters:	str date
	Type: Date
	Description: Input date.
Return value:	Type: String
	Description: Date string.

Date.toLocaleString
Description:	Converts given date to locale string.
Parameters:	str date
	Type: Date
	Description: Input date.
Return value:	Type: String
	Description: Date string.

Date.fromString
Description:	Converts string to date.
Parameters:	Name: dateStr
	Type: String
	Description: Input string.
Return value:	Type: Date
	Description: Date

Date.getYear
Description:	Get year from date.
Parameters:	Name: date
	Type: Date
	Description: Input date.
Return value:	Type: Integer
	Description: Year

Date.getMonth
Description:	Get month from date (1 to 12).
Parameters:	Name: date
	Type: Date
	Description: Input date.
Return value:	Type: Integer
	Description: Year

Date.getDay
Description:	Get day of the month from date (1 to 31).
Parameters:	Name: date
	Type: Date
	Description: Input date.
Return value:	Type: Integer
	Description: Day

Date.getHours
Description:	Get hours from date (0 to 23).
Parameters:	Name: date
	Type: Date
	Description: Input date.
Return value:	Type: Integer
	Description: Hours

Date.getMinutes
Description:	Get minutes from date (0 to 59).
Parameters:	Name: date
	Type: Date
	Description: Input date.
Return value:	Type: Integer
	Description: Minutes

Date.getSeconds
Description:	Get seconds from date (0 to 59).
Parameters:	Name: date
	Type: Date
	Description: Input date.
Return value:	Type: Integer
	Description: Seconds

Date.getMilliseconds
Description:	Get milliseconds from date (0 to 999).
Parameters:	Name: date
	Type: date
	Description: Input date.
Return value:	Type: Integer
	Description: Milliseconds

Date.make
Description:	Make a date from arguments.
Parameters:	Name: year	Type: Integer	Description: Year
	Name: month	Type: Integer	Description: Month
	Name: day	Type: Integer	Description: Day
	Name: hours	Type: Integer	Description: Hours
	Name: minutes	Type: Integer	Description: Minutes
	Name: seconds	Type: Integer	Description: Seconds
	Name: milliseconds	Type: Integer	Description: Milliseconds
Return value:	Type: Date
	Description: Constructed date.

### Math
Math.sin
Description:	Returns the sine of a number in radians.
Parameters:	Name: x
	Type: Integer|Float|Double.
	Description: A number representing an angle in radians.
Return value:	Type: Float|Double
	Description: The sine of x, between -1 and 1, inclusive.

Math.cos
Description:	Returns the cosine of a number in radians.
Parameters:	Name: x
	Type: Integer|Float|Double
	Description: A number representing an angle in radians.
Return value:	Type: Float|Double
	Description: The cosine of x, between -1 and 1, inclusive.

Math.pow
Description:	Returns the value of a base raised to a power.
Parameters:	Name: base	Type: Integer|Float|Double	Description: The base number.
	Name: exponent	Type: Integer|Float|Double	Description: The exponent number.
Return value:	Type: Float|Double
	Description: A number representing base taken to the power of exponent.

Math.log
Description:	Returns the natural logarithm (base e) of a number.
Parameters:	Name: x
	Type: Integer|Float|Double
	Description: A number greater than or equal to 0.
Return value:	Type: Float|Double
	Description: The natural logarithm (base e) of x.

Math.log10
Description:	Returns the base 10 logarithm of a number.
Parameters:	Name: x
	Type: Integer|Float|Double
	Description: A number greater than or equal to 0.
Return value:	Type: Float|Double
	Description: The base 10 logarithm of x.

Math.abs
Description:	Returns the absolute value of a number.
Parameters:	Name: x
	Type: Integer|Float|Double
	Description: A number.
Return value:	Type: Integer|Float|Double
	Description: The absolute value of x. If x is negative (including -0), returns -x. Otherwise, returns x. The result is therefore always a positive number or 0.

Math.floor
Description:	Always rounds down and returns the largest integer less than or equal to a given number.
Parameters:	Name: x
	Type: Integer|Float|Double
	Description: A number.
Return value:	Type: Integer|Float|Double
	Description: The largest integer smaller than or equal to x. / It’s the same value as -Math.ceil(-x).

Math.ceil
Description:	Always rounds up and returns the smaller integer greater than or equal to a given number.
Parameters:	Name: x
	Type: Integer|Float|Double
	Description: A number.
Return value:	Type: Integer|Float|Double
	Description: The smallest integer greater than or equal to x. / It’s the same value as -Math.floor(-x).

Math.round
Description:	Returns the value of a number rounded to the nearest integer.
Parameters:	Name: value
	Type: Integer|Float|Double
	Description: A number.
Return value:	Type: Integer|Float|Double
	Description: The value of x rounded to the nearest integer.

Math.min
Description:	Returns the smallest of the numbers given as input parameters.
Parameters:	Name: value1, …, valueN
	Type: Integer|Float|Double
	Description: Zero or more numbers among which the lowest value will be selected and returned.
Return value:	Type: Integer|Float|Double
	Description: The smallest of the given numbers.

Math.max
Description:	Returns the largest of the numbers given as input parameters.
Parameters:	Name: value1, …, valueN
	Type: Integer|Float|Double
	Description: Zero or more numbers among which the largest value will be selected and returned.
Return value:	Type: Integer|Float|Double
	Description: The largest of the given numbers.

### String
String.length
Description:	Returns the length of the string.
Parameters:	Name: string
	Type: String
	Description: A string.
Return value:	Type: Integer
	Description: The length of a string.

String.substring
Description:	Returns the part of the string from the start index up to and excluding the end index, or to the end of the string if no end index is supplied.
Parameters:	Name: string		Type: String	Description: A string.
	Name: start		Type: String	Description: The index of the first character to include in the returned substring.
	Name: end	Optional: Yes	Type: String	Description: The index of the first character to exclude from the returned substring.
Return value:	Type: String
	Description: A new string containing the specified part of the given string.

String.find
Description:	Searches a string and returns the index of the first occurrence of the specified substring.
Parameters:	Name: string	Type: String	Description: A string.
	Name: substring	Type: String	Description: Substring to search for.
Return value:	Type: String
	Description: The index of the first occurrence of substring found, or -1 if not found.

String.padStart
Description:	Pads the current string with another string (multiple times, if needed) until the resulting string reaches the given length.
Parameters:	Name: string	Type: String	Description: A string.
	Name: targetLength	Type: Integer	Description: The length of the resulting string once the current str has been padded. If the value is less than or equal to str.length, then str is returned as-is.
	Name: padString	Type: String	Description: The string to pad the current str with. If padString is too long to stay within the targetLength, it will be truncated from the end.
Return value:	Type: String
	Description: A String of the specified targetLength with padString applied from the start.

String.split
Description:	Takes a separator parameter and divides a String into an ordered list of substrings by searching for the separator pattern, puts these substrings into an array, and returns the array.
Parameters:	Name: string	Type: String	Description: A string.
	Name: separator	Type: Integer	Description: The pattern describing where each split should occur.
Return value:	Type: array:string
	Description: An Array of strings, split at each point where the separator occurs in the given string.

### Array
Array.length
Description:	The number of elements in given array.
Parameters:	Name: array
	Type: Array
	Description: An array.
Return value:	Type: Integer
	Description: The length of an array.

Array.slice
Description:	Returns a shallow copy of a portion of an array into a new array object selected from start to end (end not included) where start and end represent the index of items in that array. The original array will not be modified.
Parameters:	Name: array		Type: Array	Description: An array.
	Name: start		Type: Integer	Description: Zero-based index at which to start extraction.
	Name: end	Optional: Yes	Type: Integer	Description: Zero-based index at which to end extraction.
Return value:	Type: Array
	Description: A new array containing the extracted elements.

Array.allocate
Description:	Creates a new array of given size.
Parameters:	Name: size
	Type: Array
	Description: A size number.
Return value:	Type: Array
	Description: A new array.

Array.append
Description:	To an existing array appends an element to the end and returns a new array. The original array will not be modified.
Parameters:	Name: array	Type: Array	Description: An array.
	Name: value	Type: any	Description: Element value to be appended.
Return value:	Type: Array
	Description: A new array with appended element.

Array.insert
Description:	To an existing array inserts an element at given position and returns a new array. The original array will not be modified.
Parameters:	Name: array	Type: Array	Description: An array.
	Name: position	Type: Integer	Description: Zero-based index at which new element will be inserted.
	Name: value	Type: any	Description: Element value to be inserted.
Return value:	Type: Array
	Description: A new array with inserted element.

Array.remove
Description:	From an existing array removes an element at given position and returns a new array. The original array will not be modified.
Parameters:	Name: array	Type: Array	Description: An array.
	Name: position	Type: Integer	Description: Zero-based index from which existing element will be inserted.
Return value:	Type: Array
	Description: A new array with element removed.

Array.clone
Description:	Deep clone of the array.
Parameters:	Name: array
	Type: Array
	Description: An array.
Return value:	Type: Array
	Description: A new array.

### LVGL
LVGL.MeterTickIndex
Description:	See the LVGL Meter Widget description (Chapter XX) for the purpose of this function.
Parameters:	None
Return value:	Type: Integer
	Description: Index number.

## Expression Builder
Expressions are supported in both Action and Widget components. Each property of component that can be evaluated from the expression has "..." icon which opens Expression Builder (Fig. 5). Expressions can be entered manually or using the Expression Builder.

Fig. 5: Expression builder