# Bitmap (EEZ-GUI)
## Description
This Widget displays a bitmap.

## Properties

Specific
### Data EXPRESSION (integer) / Index of the bitmap to be displayed. It is necessary to use the functions Flow.getBitmapIndex({<bitmapName>}), which receives bitmapName, i.e. the name of the bitmap, and returns the index of the bitmap. In this way, we can choose or change which bitmap will be displayed in the runtime, because, for example, `bitmapName' can come from a variable. / ### Bitmap ObjectReference / The name of the bitmap to be displayed. / ### Visible EXPRESSION (boolean) / If the calculated expression is true then the Widget is visible, and if it is false then the Widget is hidden. It can be left blank, in which case the Widget is always visible.

Position and size
### Resizing Any / If the page where this Widget is located has the "Scale to fit" option enabled, then this option can be used to control how the position and size of the widget will be calculated when scaling the page: / With the Pin to edge option we can fix the top, right, bottom and left edge of the Widget in relation to the page when it changes its original dimension because the Scale to fit option is selected. E.g. if we selected Pin to top edge then the distance between the top edge of the page and the top edge of the Widget will always be the same, in other words the Top position does not change the value. If Pin to top edge is not selected, then the Top position will scale proportionally as the page height scales. / Using the Fix size option, we can fix the width/height of the Widget, i.e. if this option is selected the width/height will always be the same, and if not selected the width/height will scale proportionally as the page height scales. / Note: If Pin to left edge and Pin to right edge are selected, then the Fix width option will be disabled, and conversely if Fix width is selected, then both Pin to left edge and Pin to right edge cannot be selected, because both cannot be satisfied. The same applies to Pin to top edge and Pin to bottom edge and Fix width. / ### Hide "Widget is outside of its parent" warning Boolean / Check when we want to hide "Widget is outside of its parent" warning message(s). / ### Align and distribute Any / Alignment icons and component distribution. Alignment icons appear when two or more components are selected, and distribution icons appear when three or more components are selected. / ### Center widget Any / Icons for horizontal and vertical centering of widgets within a page or parent widget. / ### Left Number / X position of the component in relation to the page or parent widget. It is set in pixels. / Hint: when setting the value of this property (as well as the Top, Width and Height properties), simple mathematical expressions can be used. When we enter an expression and press enter, the expression will be evaluated and the result set as the value of this property. It is allowed to use +, -, * and / operators in expressions. Brackets can also be used. / Examples of such mathematical expressions: 18 + 36, 50 + 32 * 6, (100 - 32) / 2. / ### Top Number / Y position of the component in relation to the page or parent widget. It is set in pixels. / ### Width Number / The width of the component. It is set in pixels. / ### Height Number / The height of the component. It is set in pixels. / ### Absolute position String / The absolute position of the component in relation to the page. This property is read-only.

Style
### Default Object / Style used when rendering the background of the Widget.

Events
### Event handlers Array / List of event handler definitions. During execution, the widget can generate certain events (e.g. the CLICKED event is generated when the touchscreen is pressed and released within the Widget) and through this list we can specify the method of event processing. We must define these properties for each event handler: / Event – Event that is processed, e.g. CLICKED. / Handler type – There are two options: Flow or Action. If Flow is selected, a flow output will be added through which the event is processed, and if Action is selected, then it is necessary to specify which User action will be performed during event processing. / Action - If the Handler type is set to Action, then here we need to enter the name of the User action that will be performed during the processing of the selected event.

Flow
### Inputs Array / Additional component inputs that the user can add as desired in order to use them to receive additional data needed when evaluating expressions in properties. Each input is given a name and type. Name is used when referencing an input within an expression. A type is used to project Check to check whether a data line that transmits data of that type is connected to the input or not. / ### Outputs Array / Additional component outputs that the user can add to send data through. Each output is assigned a name and type. An example of using this output is e.g. in the Loop component, where we can put the output name for the Variable property instead of e.g. variable name. In that case, the Loop component will not change the content of the variable in each step, but will send the current value through that output. / ### Catch error Boolean / If this checkbox is enabled then an @Error output will be added to the component and if an error occurs in this component during the execution of the Flow, the Flow will continue through that output. The data that will be passed through that output is the textual description of the error.

## Examples

eez-gui-widgets-demo