# WriteSetting
## Description

This Action will add the set Key to the .eez-project-runtime-settings file (it's the same file where persistent variables are saved), or it will update the value with Value of that key if it already exists.
NOTE: WriteSetting and ReadSetting Actions are used to save and retrieve from the eez-project-runtime-settings file all those settings that we want to survive the Dashboard project restart. It is more convenient to use persistent variables, because in that case we do not have to execute a special Action for saving and retrieving.
## Properties

Specific
### Key EXPRESSION (string) / A string containing the name of the key to be added/updated. / ### Value EXPRESSION (any) / The value of the key that will be created or updated.

General
### Description String / This is the description of the Action component. Description is displayed below the component in the Project editor/viewer. In the main toolbar, it is possible to hide or display descriptions of all components with one click.

Flow
### Inputs Array / Additional component inputs that the user can add as desired in order to use them to receive additional data needed when evaluating expressions in properties. Each input is given a name and type. Name is used when referencing an input within an expression. A type is used to project Check to check whether a data line that transmits data of that type is connected to the input or not. / ### Outputs Array / Additional component outputs that the user can add to send data through. Each output is assigned a name and type. An example of using this output is e.g. in the Loop component, where we can put the output name for the Variable property instead of e.g. variable name. In that case, the Loop component will not change the content of the variable in each step, but will send the current value through that output. / ### Catch error Boolean / If this checkbox is enabled then an @Error output will be added to the component and if an error occurs in this component during the execution of the Flow, the Flow will continue through that output. The data that will be passed through that output is the textual description of the error.

Position and size
### Align and distribute Any / Alignment icons and component distribution. Alignment icons appear when two or more components are selected, and distribution icons appear when three or more components are selected.

## Inputs
### seqin SEQ | OPTIONAL
A standard sequence input.

## Outputs
### seqout SEQ | OPTIONAL
A standard sequence output.