# Variables
A variable stores data that can be changed later on. Project with Flow support can have both global and local variables. Global variables are visible from all Flows, local variables are visible only inside the Flow in which it is defined.

Project without Flow support can have only global variables and those variables must be Native i.e. variables managed by the native code (written in C++).

To add variables, use the Variables panel (Fig. 1), when a dialog box will open for defining the basic parameters of the variable (Name, Type and Default value).

To edit the parameters of the variable selected in the Variables panel, use the Properties panel. In Fig. 2, Fig. 3 and Fig. 4 shows Properties panels for different types of variables from different types of projects.

Fig. 1: Variables panel	Fig. 2: Variable Properties panel (EEZ-GUI)

Fig. 3: Variable Properties panel (LVGL)	Fig. 4: Variable Properties panel (Dashboard)

Item	Description
Id	ID is EEZ-GUI project specific and is used in Page, Action, Global Variable, Style, Font, Bitmap and Colors. These are all resources that are referenced by name in the project editor. When that project is built, names are no longer used, but numerical IDs. This field is optional, i.e. an ID does not have to be specified, in which case an ID will be assigned during the build. However, if we want an object to always get the same ID, then it needs to be defined. Why would we want to always have the same ID? This is necessary when there is a master project such as modular-psu-firmware.eez-project from EEZ BB3 and that master project is used by BB3 Applets and BB3 MicroPython scripts and they can use resources from the master project that have that ID defined. / Important: once the ID is set, it should not be changed, otherwise all BB3 scripts that depend on it should be rebuilt.
Name	Variable is referenced in other parts of project by its name. / Rules for naming variables: Starts with a letter or an underscore (_), followed by zero or more letters, digits, or underscores. Spaces are not allowed.
Description	Optional field, contains a description of the variable.
Type	The type of data stored in variable. When adding a new variable, its suggested default value will depend on the selected type (0 for Integer, False for Boolean, etc.).
Native	The variable is managed by the native code (written in C++). / A Dashboard project cannot have Native variables, and working with them is explained in Chapter XX.
Default value	Default value is the initial value of the variable when Flow starts. Given in JSON notation (https://www.json.org/json-en.html). / For example: 123, "Hello", true / If types is struct: { "member1": 42, "member2": "Hello" } / If type is array: [1, 2, 3] or ["string1", "string2", "string3"]
Default value list	Only supported in EEZ-GUI project that does not have EEZ Flow enabled.
Used in	See Configurations (Chapter P13.2.1) in project Settings.
Persistent (Global variables only)	Stores the last value of the variable in the .eez-runtime-settings file, so that next time projects will have this value, instead of the default value. / Supported only in Dashboard projects.

## Variables usage in the project with EEZ Flow enabled
Data stored in a variable can be accessed using expressions. The following Action components are used to work with variables:
- Evaluate – evaluates expression, which can use variables, and sends the result through "result" data line.
- Watch – monitors the change in the value of the variable. At Flow start, it always sends the current value via the Changed data flow line, and later every value change is sent.
- SetVariable – sets a new variable value. Multiple entries are allowed. Each entry contains a variable and an expression field. During Flow execution, the evaluated expression will be stored in a variable.
- SwitchCase, Compare, IsTrue – Actions used for branching in the Flow depending on the value of the variable
Variables are also used in Widget components. Certain Widget properties can be defined as an expression. In this case, the value of that property will change during Flow execution as the expression changes. For example, Label widget can show the content of some variable, and it will updated every time this variable has been modified.

## Variable types
### Basic/Primitive types
Item	Description
Integer	Signed 32-bit integer.
Float	IEEE 4-byte floating-point.
Double	IEEE 8-byte floating-point.
Boolean	Can hold true of false value.
String	Sequence of characters.
Date	Unix timestamp.
Blob	Binary large object (Dashboard projects only).
Stream	Stream of data (Dashboard projects only).
Any	Can hold any data type.

### Structures
Structure types are defined in Variables panel in Structs section. Struct type variable stores multiple data values each accessed by its member name. Each member is defined by its name and type.

Structures can only be used in projects that have EEZ Flow enabled.
### Enums
Enums types are defined in Variables panel in Enums section. Enum type variable stores integer data value, but can contain only restricted set of values. Each enum member is defined by its name and integer value.
### Objects
Object variables, similar to structs, can hold multiple values, each accessed by member names. The member names depends of the type of Object variable. Example of object variables: Instrument connection or PostgreSQL connection. Object variables are described in more detail in Chapter XX.

Object variables can only be used in Dashboard projects.
### Arrays
Array variable stores multiple data values.
### Expressions
An expression contains instructions on how to evaluate a data value during Flow execution. An expression is defined in code similar to JavaScript or other C-like languages.

Expression element	Description / Example
Literal value	Example: 42, "Hello", true
Variable names	Example: my_var
Input names	Retrieves the data stored in data input using the name of that input. / Example: input_name
Binary operator	Example: my_integer_var + 1
Logical operator	Example: my_integer_var < 10
Unary operator	Example: -my_integer_var
Ternary operator	Example: my_integer_var == 1 ? true : false / (evaluates to true if my_integer_var is 1, otherwise evaluates to false)
Function calls	Example: String.length(my_string_var)
Parentheses “()”	Specifying the order of the evaluation / Example: "Counter: " + (a + 1)
Accessor “.”	Structure type member accessor by using “.” / Example: my_struct_var.member1
Accessor “[]”	Array element accessor by using “[]” / Example: my_array_var[3], my_array_var[index]
Enum value	Example: MyEnumTypeName.Member1

Expression examples:

`var[i].member1`
	`var` is array which contains structs, which has member `member1`
	`i` is integer variable
	evaluates to `member1` value in the i-th element

`var == State.START || var == State.EMPTY`
	var is of type enum:State, and State enum has two members: START and EMPTY
	evaluates to True if var contains data that is either State.START or State.EMPTY

### Literals
Type	Description / Example
Integer	`42`
Float or double	`3.14`
String	`"Hello world!"`
Translated string	T"text_resource_id" (prefix T is mandatory)
Boolean	`true` or `false`
JSON	See https://www.json.org/json-en.html

### Binary Operators
Each binary operators requires two arguments. Binary operator is written between arguments, for example: <arg1> + <arg2>

#### Addition +
Rules:
- If any of the arguments is a string then result is a string. For example, `voltage +" V"` will evaluate to `"1.5 V"` if data stored in voltage variable is `1.5`
- If any of the arguments is a double then result is a double.
- If one argument is a float and the other is a float or an integer the result will be a float.
- If both arguments are integers then result is an integer.

arg1\arg2	integer	float	double	string	boolean	other_type
integer	integer	float	double	string	integer	err
double	double	double	double	string	double	err
float	float	float	double	string	float	err
string	string	string	string	string	string	err
boolean	integer	float	double	string	integer	err
other_type	err	err	err	err	err	err

#### Subtraction -
arg1\arg2	integer	float	double	boolean	other_type
integer	integer	float	double	integer	err
double	double	double	double	double	err
float	float	float	double	float	err
boolean	integer	float	double	integer	err
other_type	err	err	err	err	err

#### Multiplication *
arg1\arg2	integer	float	double	boolean	other_type
integer	integer	float	double	integer	err
double	double	double	double	double	err
float	float	float	double	float	err
boolean	integer	float	double	integer	err
other_type	err	err	err	err	err

#### Division /
arg1\arg2	integer	float	double	boolean	other_type
integer	integer	float	double	integer	err
double	double	double	double	double	err
float	float	float	double	float	err
boolean	double	float	double	double	err
other_type	err	err	err	err	err

#### Remainder %
arg1\arg2	integer	float	double	boolean	other_type
integer	integer	float	double	integer	err
double	double	double	double	double	err
float	float	float	double	float	err
boolean	integer	float	double	integer	err
other_type	err	err	err	err	err

#### Left shift <<
arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

#### Right shift >>
arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

#### Binary AND &
arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

#### Binary OR |
arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

#### Binary XOR ^
arg1\arg2	integer	boolean	other_type
integer	integer	integer	err
boolean	integer	integer	err
other_type	err	err	err

### Logical operators
Logical operators are also binary operators that result in Boolean values.

Type	Description
==	Equal to
!=	Not equal
<	Greater than
>	Less than
<=	Less than or equal to
>=	Greater than or equal to
&&	And
||	Or

### Unary operators
Type	Description
-	Negate the value
~	Binary invert
!	Logical invert

### Conditional (ternary) operator
The conditional (ternary) operator is the only operator that takes three operands: a condition followed by a question mark (?), an expression to be executed if the condition is true followed by a colon (:), and finally an expression to be executed if the condition is false.
## Functions
### System
#### System.getTick
Retrieves the number of milliseconds that have elapsed since the flow execution was started.

Parameters
None

Return value
Value in milliseconds. Return type is Integer.
### Flow
#### Flow.index
Index of current element in the List and Grid widget. Check the description of these two widget for the more information.

Parameters
Name	Type	Description
index	Integer	In case of nested List/Grid widgets use 0 for inner most List/Grid, 1 for List/Grid one up, etc.

Return value
Element index. Return type is Integer.

#### Flow.isPageActive
If this function is executed inside the page it will return true if that page is currently active page, otherwise it will return false.

Parameters
None

Return value
True if page is active, False if page is not active. Return type is Boolean.

#### Flow.pageTimelinePosition
If this function is executed inside the page or custom widget it will return the current position at the animation timeline for that page or custom widget.

Parameters
None

Return value
Timeline position. Return type is Boolean.

#### Flow.makeValue
Creates a new value of type Struct.

Parameters
Name	Type	Description
structName	String	Structure name.
value	JSON	Structure name.

Return value
Created struct value. Return type is Struct.

#### Flow.makeArrayValue
Creates a new value of type array.

Parameters
Name	Type	Description
value	JSON	Array value.

Return value
Created array value. Return type is Array.

#### Flow.languages
Retrieves a list of languages defined in multi-language project as array of strings.

Parameters
None

Return value
Array of languages. Return type is Array:string.

#### Flow.translate
Translate text resource ID, same as T"textResourceID".

Parameters
Name	Type	Description
textResourceID	String	Text resource ID.

Return value
Translated string. Return type is String.

#### Flow.parseInteger
Parse integer value given as string.

Parameters
Name	Type	Description
str	String	Input string.

Return value
Parsed integer value. Return type is Integer.

#### Flow.parseFloat
Parse float value given as string.

Parameters
Name	Type	Description
str	String	Input string.

Return value
Parsed float value. Return type is Float.

#### Flow.parseDouble
Parse double value give as string.

Parameters
Name	Type	Description
str	String	Input string.

Return value
Parsed double value. Return type is Double.

### Date
#### Date.now
Returns current date.

Parameters
None

Return value
Current datetime. Return type is Now.

#### Date.toString
Converts given date to string.

Parameters
Name	Type	Description
str date	Date	Input date.

Return value
Date string. Return type is String.

#### Date.toLocaleString
Converts given date to locale string.

Parameters
Name	Type	Description
str date	Date	Input date.

Return value
Date string. Return type is String.

#### Date.fromString
Converts string to date.

Parameters
Name	Type	Description
dateStr	String	Input string.

Return value
Date. Return type is Date.

#### Date.getYear
Get year from date.

Parameters
Name	Type	Description
date	Date	Input date.

Return value
Year. Return type is Integer.

#### Date.getMonth
Get month from date (1 to 12).

Parameters
Name	Type	Description
date	Date	Input date.

Return value
Month. Return type is Integer.

#### Date.getDay
Get day of the month from date (1 to 31).

Parameters
Name	Type	Description
date	Date	Input date.

Return value
Day. Return type is Integer.

#### Date.getHours
Get hours from date (0 to 23).

Parameters
Name	Type	Description
date	Date	Input date.

Return value
Hours. Return type is Integer.

#### Date.getMinutes
Get minutes from date (0 to 59).

Parameters
Name	Type	Description
date	Date	Input date.

Return value
Minutes. Return type is Integer.

#### Date.getSeconds
Get seconds from date (0 to 59).

Parameters
Name	Type	Description
date	Date	Input date.

Return value
Seconds. Return type is Integer.

#### Date.getMilliseconds
Get milliseconds from date (0 to 999).

Parameters
Name	Type	Description
date	Date	Input date.

Return value
Milliseconds. Return type is Integer.

#### Date.make
Make a date from arguments.

Parameters
Name	Type	Description
year	Integer	Year
month	Integer	Month
day	Integer	Day
hours	Integer	Hours
minutes	Integer	Minutes
seconds	Integer	Seconds
milliseconds	Integer	Milliseconds

Return value
Constructed date. Return type is Date.
### Math
#### Math.sin
Returns the sine of a number in radians.

Parameters
Name	Type	Description
x	Integer|Float|Double	A number representing an angle in radians.

Return value
The sine of x, between -1 and 1, inclusive. Return type is Float|Double.

#### Math.cos
Returns the cosine of a number in radians.

Parameters
Name	Type	Description
x	Integer|Float|Double	A number representing an angle in radians.

Return value
The cosine of x, between -1 and 1, inclusive. Return type is Float|Double.

#### Math.pow
Returns the value of a base raised to a power.

Parameters
Name	Type	Description
base	Integer|Float|Double	Year
exponent	Integer|Float|Double	Month

Return value
A number representing base taken to the power of exponent. Return type is Float|Double.

#### Math.log
Returns the natural logarithm (base e) of a number.

Parameters
Name	Type	Description
x	Integer|Float|Double	A number greater than or equal to 0.

Return value
The natural logarithm (base e) of x. Return type is Float|Double.

#### Math.log10
Returns the base 10 logarithm of a number.

Parameters
Name	Type	Description
x	Integer|Float|Double	A number greater than or equal to 0.

Return value
The base 10 logarithm of x. Return type is Float|Double.

#### Math.abs
Returns the absolute value of a number.

Parameters
Name	Type	Description
x	Integer|Float|Double	A number.

Return value
The absolute value of x. If x is negative (including -0), returns -x. Otherwise, returns x. The result is therefore always a positive number or 0. Return type is Integer|Float|Double.

#### Math.floor
Always rounds down and returns the largest integer less than or equal to a given number.

Parameters
Name	Type	Description
x	Integer|Float|Double	A number.

Return value
The largest integer smaller than or equal to x. It’s the same value as -Math.ceil(-x). Return type is Integer|Float|Double.

#### Math.ceil
Always rounds up and returns the smaller integer greater than or equal to a given number.

Parameters
Name	Type	Description
x	Integer|Float|Double	A number.

Return value
The smallest integer greater than or equal to x. It’s the same value as -Math.floor(-x). Return type is Integer|Float|Double.

#### Math.round
Returns the value of a number rounded to the nearest integer.

Parameters
Name	Type	Description
x	Integer|Float|Double	A number.

Return value
The value of x rounded to the nearest integer. Return type is Integer|Float|Double.

#### Math.min
Returns the smallest of the numbers given as input parameters.

Parameters
Name	Type	Description
value1, …, valueN	Integer|Float|Double	Zero or more numbers among which the lowest value will be selected and returned.

Return value
The smallest of the given numbers. Return type is Integer|Float|Double.

#### Math.max
Returns the largest of the numbers given as input parameters.

Parameters
Name	Type	Description
value1, …, valueN	Integer|Float|Double	Zero or more numbers among which the largest value will be selected and returned.

Return value
The largest of the given numbers. Return type is Integer|Float|Double.
### String
#### String.length
Returns the length of the string.

Parameters
Name	Type	Description
string	String	A string.

Return value
The length of a string. Return type is Integer.

#### String.substring
Returns the part of the string from the start index up to and excluding the end index, or to the end of the string if no end index is supplied.

Parameters
Name	Optional	Type	Description
string		String	A string.
start		String	The index of the first character to include in the returned substring.
end	Yes	String	The index of the first character to exclude from the returned substring.

Return value
A new string containing the specified part of the given string. Return type is String.

#### String.find
Searches a string and returns the index of the first occurrence of the specified substring.

Parameters
Name	Type	Description
string	String	A string.
substring	String	Substring to search for.

Return value
The index of the first occurrence of substring found, or -1 if not found. Return type is String.

#### String.padStart
Pads the current string with another string (multiple times, if needed) until the resulting string reaches the given length.

Parameters
Name	Type	Description
string	String	A string.
targetLength	Integer	The length of the resulting string once the current str has been padded. If the value is less than or equal to str.length, then str is returned as-is.
padString	String	The string to pad the current str with. If padString is too long to stay within the targetLength, it will be truncated from the end.

Return value
A String of the specified targetLength with padString applied from the start. Return type is String.

#### String.split
Takes a separator parameter and divides a String into an ordered list of substrings by searching for the separator pattern, puts these substrings into an array, and returns the array.

Parameters
Name	Type	Description
string	String	A string.
separator	Integer	The pattern describing where each split should occur.

Return value
An Array of strings, split at each point where the separator occurs in the given string. Return type is Array:string.
### Array
#### Array.length
The number of elements in given array.

Parameters
Name	Type	Description
array	Array	An array.

Return value
The length of an array. Return type is Integer.

#### Array.slice
Returns a shallow copy of a portion of an array into a new array object selected from start to end (end not included) where start and end represent the index of items in that array. The original array will not be modified.

Parameters
Name	Optional	Type	Description
array		Array	An array.
start		Integer	Zero-based index at which to start extraction.
end	Yes	Integer	Zero-based index at which to end extraction.

Return value
A new array containing the extracted elements. Return type is Array.

#### Array.allocate
Creates a new array of given size.

Parameters
Name	Type	Description
size	Array	A size number.

Return value
A new array. Return type is Array.

#### Array.append
Takes a separator parameter and divides a String into an ordered list of substrings by searching for the separator pattern, puts these substrings into an array, and returns the array.

Parameters
Name	Type	Description
array	Array	An array.
value	Any	Element value to be appended.

Return value
A new array with appended element. Return type is Array.

#### Array.insert
Inserts an element to an existing array at given position and returns a new array. The original array will not be modified.

Parameters
Name	Type	Description
array	Array	An array.
position	Integer	Zero-based index at which new element will be inserted.
value	Any	Element value to be inserted.

Return value
A new array with inserted element. Return type is Array.

#### Array.remove
Removes from an existing array an element at given position and returns a new array. The original array will not be modified.

Parameters
Name	Type	Description
array	Array	An array.
position	Integer	Zero-based index from which existing element will be inserted.

Return value
A new array with element removed. Return type is Array.

#### Array.clone
Deep clone of the array.

Parameters
Name	Type	Description
array	Array	An array.

Return value
A new array. Return type is Array.
### LVGL
#### LVGL.MeterTickIndex
See the LVGL Meter Widget description (Chapter W33) for the purpose of this function.

Parameters
None

Return value
Index number. Return type is integer.
## Expression Builder
Expressions are supported in both Action and Widget components. Each property of component that can be evaluated from the expression has "..." icon which opens Expression Builder (Fig. 5). Expressions can be entered manually or using the Expression Builder.

Fig. 5: Expression builder