# CollectStream
## Description
Concatenates a stream into a string. As data from the stream comes in chunks, they are concatenated into a string and sent to the data output. During the stream lifetime, this Action can repeatedly send the currently collected string through data. Flow execution continues through the seqout output when the stream is closed.

## Properties

Specific
### Stream EXPRESSION (any) / A stream whose content will be concatenated into a string.

General
### Description String / This is the description of the Action component. Description is displayed below the component in the Project editor/viewer. In the main toolbar, it is possible to hide or display descriptions of all components with one click.

Flow
### Inputs Array / Additional component inputs that the user can add as desired in order to use them to receive additional data needed when evaluating expressions in properties. Each input is given a name and type. Name is used when referencing an input within an expression. A type is used to project Check to check whether a data line that transmits data of that type is connected to the input or not. / ### Outputs Array / Additional component outputs that the user can add to send data through. Each output is assigned a name and type. An example of using this output is e.g. in the Loop component, where we can put the output name for the Variable property instead of e.g. variable name. In that case, the Loop component will not change the content of the variable in each step, but will send the current value through that output. / ### Catch error Boolean / If this checkbox is enabled then an @Error output will be added to the component and if an error occurs in this component during the execution of the Flow, the Flow will continue through that output. The data that will be passed through that output is the textual description of the error.

Position and size
### Align and distribute Any / Alignment icons and component distribution. Alignment icons appear when two or more components are selected, and distribution icons appear when three or more components are selected.

## Inputs
### seqin SEQ | OPTIONAL
A standard sequence input.

## Outputs
### seqout SEQ | OPTIONAL
A standard sequence output. Flow execution continues through this output after the stream is closed.

### data DATA(string) | MANDATORY
The concatenated string is sent through this output. During the stream lifetime, a string can be sent several times, which will contain all the data collected until then (i.e. the string will grow over time as new data arrives).

## Examples

RegExp Stream