# LVGL
## Description
Performs one or more LVGL specific actions.

## Properties

Specific
### Actions Array / List of actions to be executed. The following actions are available: / Change Screen Changes the active page. The following options are available: / Previous screen - if it is checked, it will go to the previous screen, otherwise you should select the page you want to display. / Screen - name of the page to be displayed. / Fade mode' - selection of animation when moving from the previous page to a new page. The following options are available: / None - switch immediately after delay ms / Over left / Over right / Over top / Over bottom - move the new page over the others towards the given direction. / Move Left/Right/Top/Bottom - move both the old and new pages towards the given direction. / Fade in / Fade out - fade the new page over the old page, or vice versa. / Out left / Out right / Out top / Out bottom - move out the old page over the current one towards the given direction. / Speed - animation duration in milliseconds. / Delay - delay in milliseconds before the animation starts. / Play Animation Animates the selected Widget property. The following options are available: / Target - Widget whose property is animated / Property - Widget property that is animated. / Start - initial property value. / End - the final value of the property. / Delay - delay in milliseconds before the animation starts. / Time - the total duration of the animation in milliseconds. / Relative - determines whether Start and End values are relative to the current value or are absolute values. / Instant - if checked apply the start value immediately, otherwise apply the start value after a delay when the animation really starts. / Path - determines the animation curve. The following options are available: / Linear - calculate the current value of an animation applying linear characteristic / Ease in - calculate the current value of an animation slowing down the start phase / Ease out - calculate the current value of an animation slowing down the end phase / Ease in out - calculate the current value of an animation applying an "S" characteristic (cosine) / Overshoot - calculate the current value of an animation with overshoot at the end / Bounce - calculate the current value of an animation with 3 bounces / Set Property Changes the value of the selected property for the selected Widget. The following options are available: / Target type - The type of Widget that changes. / Target - Widget whose property is changed. / Property - the property that is being changed. / Value - new property value. / Animated - if there is a possibility to animate the property, then you can choose to make the change animated. For example for Slider, changing position slider (Value property) can be animated.

General
### Description String / This is the description of the Action component. Description is displayed below the component in the Project editor/viewer. In the main toolbar, it is possible to hide or display descriptions of all components with one click.

Flow
### Inputs Array / Additional component inputs that the user can add as desired in order to use them to receive additional data needed when evaluating expressions in properties. Each input is given a name and type. Name is used when referencing an input within an expression. A type is used to project Check to check whether a data line that transmits data of that type is connected to the input or not. / ### Outputs Array / Additional component outputs that the user can add to send data through. Each output is assigned a name and type. An example of using this output is e.g. in the Loop component, where we can put the output name for the Variable property instead of e.g. variable name. In that case, the Loop component will not change the content of the variable in each step, but will send the current value through that output. / ### Catch error Boolean / If this checkbox is enabled then an @Error output will be added to the component and if an error occurs in this component during the execution of the Flow, the Flow will continue through that output. The data that will be passed through that output is the textual description of the error.

Position and size
### Align and distribute Any / Alignment icons and component distribution. Alignment icons appear when two or more components are selected, and distribution icons appear when three or more components are selected.

## Inputs
### seqin SEQ | OPTIONAL
A standard sequence input.

## Outputs
### seqout SEQ | OPTIONAL
A standard sequence output.

## Examples

Change Screen