# MQTTSubscribe
## Description
This Action must be performed immediately after successfully connecting to the MQTT server, for each topic to which we want to subscribe. If a packet has been published by the server for this topic, we will receive information about it via the Message event using the MQTTEvent Action.

## Properties

Specific
### Connection EXPRESSION (object:MQTTConnection) / The name of the connection to the MQTT server. / ### Topic EXPRESSION (string) / The name of the topic to which we want to subscribe. A subscription may be to an explicit topic, in which case only messages to that topic will be received, or it may include wildcards. Two wildcards are available, + or #. + can be used as a wildcard for a single level of hierarchy. It could be used with the topic above to get information on all computers and hard drives as follows: / sensors/+/temperature/+ / As another example, for a topic of a/b/c/d, the following example subscriptions will match: / a/b/c/d / +/b/c/d / a/+/c/d / a/+/+/d / +/+/+/+ / The following subscriptions will not match: / a/b/c / b/+/c/d / +/+/+ / # can be used as a wildcard for all remaining levels of hierarchy. This means that it must be the final character in a subscription. With a topic of a/b/c/d, the following example subscriptions will match: / a/b/c/d / # / a/# / a/b/# / a/b/c/# / +/b/c/#

General
### Description String / This is the description of the Action component. Description is displayed below the component in the Project editor/viewer. In the main toolbar, it is possible to hide or display descriptions of all components with one click.

Flow
### Inputs Array / Additional component inputs that the user can add as desired in order to use them to receive additional data needed when evaluating expressions in properties. Each input is given a name and type. Name is used when referencing an input within an expression. A type is used to project Check to check whether a data line that transmits data of that type is connected to the input or not. / ### Outputs Array / Additional component outputs that the user can add to send data through. Each output is assigned a name and type. An example of using this output is e.g. in the Loop component, where we can put the output name for the Variable property instead of e.g. variable name. In that case, the Loop component will not change the content of the variable in each step, but will send the current value through that output. / ### Catch error Boolean / If this checkbox is enabled then an @Error output will be added to the component and if an error occurs in this component during the execution of the Flow, the Flow will continue through that output. The data that will be passed through that output is the textual description of the error.

Position and size
### Align and distribute Any / Alignment icons and component distribution. Alignment icons appear when two or more components are selected, and distribution icons appear when three or more components are selected.

## Inputs
### seqin SEQ | OPTIONAL
A standard sequence input.

## Outputs
### seqout SEQ | OPTIONAL
A standard sequence output.

## Examples

MQTT