# Bar
## Description
The bar object has a background and an indicator on it. The width of the indicator is set according to the current value of the bar.
Vertical bars can be created if the width of the object is smaller than its height.
Not only the end, but also the start value of the bar can be set, which changes the start position of the indicator.
More info (link)
## Properties

Specific
### Min Number / The minimum value that Value and Value start can contain. / ### Max Number / The maximum value that Value and Value start can contain. / ### Mode Enum / Bar mode options: / NORMAL – A normal bar. / SYMMETRICAL – Draw the indicator from the zero value to current value. Requires a negative minimum range and positive maximum range. / RANGE – Allows setting the start value (Value start property) and end value (Value property). / ### Value EXPRESSION (integer) / The end value on the bar. / ### Value type Enum / Select between Literal and Expression. If Expression is selected then Value can be evaluated from the expression. / ### Value start EXPRESSION (integer) / The start value on the bar if RANGE mode is selected. / ### Value start type Enum / Select between Literal and Expression. If Expression is selected then Value start can be evaluated from the expression.

General
### Name String / Widget name. We reference the Widget within the project by its name, for example in the LVGL action. For each Widget, we must choose a unique name within the entire project. This field is optional and does not need to be set if we do not need to reference the Widget.

Position and size
### Align and distribute Any / Alignment icons and component distribution. Alignment icons appear when two or more components are selected, and distribution icons appear when three or more components are selected. / ### Center widget Any / Icons for horizontal and vertical centering of widgets within a page or parent widget. / ### Left Number / X position of the component in relation to the page or parent widget. It is set in pixels. / Hint: when setting the value of this property (as well as the Top, Width and Height properties), simple mathematical expressions can be used. When we enter an expression and press enter, the expression will be evaluated and the result set as the value of this property. It is allowed to use +, -, * and / operators in expressions. Brackets can also be used. / Examples of such mathematical expressions: 18 + 36, 50 + 32 * 6, (100 - 32) / 2. / ### Left unit Enum / The following options are available: / px – Left is default in pixels. / % – Left is set as a percentage in relation to the parent width. / ### Top Number / Y position of the component in relation to the page or parent widget. It is set in pixels. / ### Top unit Enum / The following options are available: / px – Top is set in pixels. / % – The top is set as a percentage in relation to the parent height. / ### Width Number / The width of the component. It is set in pixels. / ### Width unit Enum / The following options are available: / px – Width is given in pixels. / % – Width is given as a percentage in relation to the parent width. / content – Width is automatically set to fit the entire content in width. / ### Height Number / The height of the component. It is set in pixels. / ### Height unit Enum / The following options are available: / px – Height is given in pixels. / % – Height is given as a percentage in relation to the parent height. / content – Height is automatically set to fit the entire content in height.

Layout
### Tab title EXPRESSION (string) / If this widget is a child of a container with layout set to Docking Manager, use this property to set the title of the tab that contains this widget.

Style
### Use style ObjectReference / Here we can select one of the globally defined Styles so that the Widget uses that Style.

Flags
### Hidden EXPRESSION (boolean) / Make the object hidden. / ### Hidden flag type Enum / Here we can choose whether the Hidden flag state will be calculated from the Expression or not. / ### Clickable EXPRESSION (boolean) / Make the object clickable by input devices. / ### Clickable flag type Enum / Here we can choose whether the Clickable flag state will be calculated from the Expression or not. / ### Click focusable Boolean / Add focused state to the object when clicked. / ### Checkable Boolean / Toggle checked state when the object is clicked. / ### Scrollable Boolean / Make the object scrollable. / ### Scroll elastic Boolean / Allow scrolling inside but with slower speed. / ### Scroll momentum Boolean / Make the object scroll further when "thrown". / ### Scroll one Boolean / Allow scrolling only one snappable children. / ### Scroll chain hor Boolean / Allow propagating the horizontal scroll to a parent. / ### Scroll chain ver Boolean / Allow propagating the vertical scroll to a parent. / ### Scroll chain Boolean / Allow propagating both the horizontal and the vertical scroll to a parent. / ### Scroll on focus Boolean / Automatically scroll object to make it visible when focused. / ### Scroll with arrow Boolean / Allow scrolling the focused object with arrow keys. / ### Snappable Boolean / If scroll snap is enabled on the parent it can snap to this object. / ### Press lock Boolean / Keep the object pressed even if the press slid from the object. / ### Event bubble Boolean / Propagate the events to the parent too. / ### Gesture bubble Boolean / Propagate the gestures to the parent. / ### Adv hittest Boolean / Allow performing more accurate hit (click) test. E.g. accounting for rounded corners. / ### Ignore layout Boolean / Make the object positionable by the layouts. / ### Floating Boolean / Do not scroll the object when the parent scrolls and ignore layout. / ### Overflow visible Boolean / Do not clip the children's content to the parent's boundary. / ### Scrollbar mode Enum / Scrollbars are displayed according to a configured mode. The following mode(s) exist: / OFF: Never show the scrollbars / ON: Always show the scrollbars / ACTIVE: Show scroll bars while an object is being scrolled / AUTO: Show scroll bars when the content is large enough to be scrolled / ### Scroll direction Enum / Controls the direction in which scrolling happens. The following mode(s) exist: / NONE: no scroll / TOP: only scroll up / LEFT: only scroll left / BOTTOM: only scroll down / RIGHT: only scroll right / HOR: only scroll horizontally / VER: only scroll vertically / ALL: scroll any directions

States
### Checked EXPRESSION (boolean) / Toggled or checked state. / ### Checked state type Enum / Here we can choose whether the Checked state will be calculated from the Expression or not. / ### Disabled EXPRESSION (boolean) / Disabled state / ### Disabled state type Enum / Here we can choose whether the Disabled state will be calculated from the Expression or not. / ### Focused Boolean / Focused via keypad or encoder or clicked via touchpad/mouse. / ### Pressed Boolean / Being pressed.

Events
### Event handlers Array / List of event handler definitions. During execution, the widget can generate certain events (e.g. the CLICKED event is generated when the touchscreen is pressed and released within the Widget) and through this list we can specify the method of event processing. We must define these properties for each event handler: / Event – Event that is processed, e.g. CLICKED. / Handler type – There are two options: Flow or Action. If Flow is selected, a flow output will be added through which the event is processed, and if Action is selected, then it is necessary to specify which User action will be performed during event processing. / Action - If the Handler type is set to Action, then here we need to enter the name of the User action that will be performed during the processing of the selected event.

Flow
### Inputs Array / Additional component inputs that the user can add as desired in order to use them to receive additional data needed when evaluating expressions in properties. Each input is given a name and type. Name is used when referencing an input within an expression. A type is used to project Check to check whether a data line that transmits data of that type is connected to the input or not. / ### Outputs Array / Additional component outputs that the user can add to send data through. Each output is assigned a name and type. An example of using this output is e.g. in the Loop component, where we can put the output name for the Variable property instead of e.g. variable name. In that case, the Loop component will not change the content of the variable in each step, but will send the current value through that output. / ### Catch error Boolean / If this checkbox is enabled then an @Error output will be added to the component and if an error occurs in this component during the execution of the Flow, the Flow will continue through that output. The data that will be passed through that output is the textual description of the error.

## Examples

Dashboard Widgets Demo