# Animate
## Description
If this action is used inside Page or User Widget, it will move the position of the animation timeline from one position (From property) to another (To property) with given speed (Speed property).
If we want to instantly jump to a certain position (To property), then we should set the Speed to 0 - in that case the From property value doesn't matter (it can be set to the same value as To property).
The expression Flow.pageTimelinePosition() can be used for the From property and in that case the animation will start from the current position.
## Properties

Specific
### From EXPRESSION (float) / Start position set in seconds. / ### To EXPRESSION (float) / End position set in seconds. / ### Speed EXPRESSION (float) / Determines the duration of the animation. If set to 1 then the animation will last From - To seconds. If we want a twice as fast animation then it should be set to 2, and if we want a twice slower animation then it should be set to 0.5. / If we want the animation to last a specific time T then the formula T / (From - To) can be used, e.g. if T is equal to 0.5 seconds, From 1 seconds and To 3 seconds, then 0.5 / (3 - 1) should be set for speed, i.e. 0.25. / If it is set to 0 then it will immediately jump to the To position during execution.

General
### Description String / This is the description of the Action component. Description is displayed below the component in the Project editor/viewer. In the main toolbar, it is possible to hide or display descriptions of all components with one click.

Flow
### Inputs Array / Additional component inputs that the user can add as desired in order to use them to receive additional data needed when evaluating expressions in properties. Each input is given a name and type. Name is used when referencing an input within an expression. A type is used to project Check to check whether a data line that transmits data of that type is connected to the input or not. / ### Outputs Array / Additional component outputs that the user can add to send data through. Each output is assigned a name and type. An example of using this output is e.g. in the Loop component, where we can put the output name for the Variable property instead of e.g. variable name. In that case, the Loop component will not change the content of the variable in each step, but will send the current value through that output. / ### Catch error Boolean / If this checkbox is enabled then an @Error output will be added to the component and if an error occurs in this component during the execution of the Flow, the Flow will continue through that output. The data that will be passed through that output is the textual description of the error.

Position and size
### Align and distribute Any / Alignment icons and component distribution. Alignment icons appear when two or more components are selected, and distribution icons appear when three or more components are selected.

## Inputs
### seqin SEQ | OPTIONAL
A standard sequence input.
## Outputs
### seqout SEQ | OPTIONAL
A standard sequence output. It is activated when the animation is finished, ie. when the To position was reached.
## Examples

- Animation
- sld-eez-flow-demo