# EEZChart
## Description

Displays a line chart using the same Widget as in the Instrument History panel.
## Properties

Specific
### Chart mode Enum / The following modes are available: / Single chart – Displays a single chart. / Multiple charts – Displays multiple charts. / EEZ DLOG – Displays the chart given by the EEZ DLOG file format. / Instrument History Item – Displays a chart from the instrument history. / ### Chart data EXPRESSION (any) / If Chart mode is set to Single chart, then a string, array or blob containing the samples that will be displayed in the chart should be set here. If Chart mode is set to EEZ DLOG then the content of the EEZ DLOG file should be set here (e.g. it can be read with FileRead Action, see EEZ Chart example). / This property is not used when the Chart mode is Multiple charts or Instrument History item. / ### Format EXPRESSION (string) / Format of Data property. Possible values: / "float" – "Chart data" must be a blob containing 32-bit, little-endian float numbers, or array:float / "double" – "Chart data" must be a blob containing 64-bit, little-endian float numbers, or array:float / "rigol-byte" – "Chart data" must be a blob containing 8-bit unsigned integer numbers / "rigol-word" – "Chart data" must be a blob containing 16-bit unsigned integer numbers / "csv" – "Chart data" must be a CSV string, the first column is taken / This property is only used when the Chart mode is Single chart. / ### Sampling rate EXPRESSION (integer) / Sampling rate or number of samples per second (SPS). / This property is only used when the Chart mode is Single chart. / ### Unit name EXPRESSION (integer) / The unit displayed on the Y-axis. The X-axis is always time. / This property is only used when the Chart mode is Single chart. / ### Color EXPRESSION (string) / The color of the line in the chart. / This property is only used when the Chart mode is Single chart. / ### Label EXPRESSION (string) / Chart label: / This property is only used when the Chart mode is Single chart. / ### Offset EXPRESSION (string) / Offset value used in formula offset + sample_value * scale which transforms sample value to sample position on y axis in the chart. / This property is only used when the Chart mode is Single chart. / ### Scale EXPRESSION (string) / When displaying samples, the formula offset + sample_value * scale is used. / This property is only used when the Chart mode is Single chart. / ### Charts Array / List of chart definitions when Chart mode is set to Multiple charts. Each definition contains these properties: / Chart data / Format / Sampling rate / Unit / Color / Label / Offset / Scale / These properties have the same meaning as the corresponding property when Single chart mode is selected. / ### History item ID EXPRESSION (string) / This ID is obtained using AddToInstrumentHistory action through id output of that action. / This property is only used when the Chart mode is Instrument History Item. / ### Visible EXPRESSION (boolean) / If the calculated expression is true then the Widget is visible, and if it is false then the Widget is hidden. It can be left blank, in which case the Widget is always visible.

Position and size
### Resizing Any / If the page where this Widget is located has the "Scale to fit" option enabled, then this option can be used to control how the position and size of the widget will be calculated when scaling the page: / With the Pin to edge option we can fix the top, right, bottom and left edge of the Widget in relation to the page when it changes its original dimension because the Scale to fit option is selected. E.g. if we selected Pin to top edge then the distance between the top edge of the page and the top edge of the Widget will always be the same, in other words the Top position does not change the value. If Pin to top edge is not selected, then the Top position will scale proportionally as the page height scales. / Using the Fix size option, we can fix the width/height of the Widget, i.e. if this option is selected the width/height will always be the same, and if not selected the width/height will scale proportionally as the page height scales. / Note: If Pin to left edge and Pin to right edge are selected, then the Fix width option will be disabled, and conversely if Fix width is selected, then both Pin to left edge and Pin to right edge cannot be selected, because both cannot be satisfied. The same applies to Pin to top edge and Pin to bottom edge and Fix width. / ### Align and distribute Any / Alignment icons and component distribution. Alignment icons appear when two or more components are selected, and distribution icons appear when three or more components are selected. / ### Center widget Any / Icons for horizontal and vertical centering of widgets within a page or parent widget. / ### Left Number / X position of the component in relation to the page or parent widget. It is set in pixels. / Hint: when setting the value of this property (as well as the Top, Width and Height properties), simple mathematical expressions can be used. When we enter an expression and press enter, the expression will be evaluated and the result set as the value of this property. It is allowed to use +, -, * and / operators in expressions. Brackets can also be used. / Examples of such mathematical expressions: 18 + 36, 50 + 32 * 6, (100 - 32) / 2. / ### Top Number / Y position of the component in relation to the page or parent widget. It is set in pixels. / ### Width Number / The width of the component. It is set in pixels. / ### Height Number / The height of the component. It is set in pixels. / ### Absolute position String / The absolute position of the component in relation to the page. This property is read-only.

Style
### Default Object / Style used when rendering of the Widget.

Events
### Event handlers Array / List of event handler definitions. During execution, the widget can generate certain events (e.g. the CLICKED event is generated when the touchscreen is pressed and released within the Widget) and through this list we can specify the method of event processing. We must define these properties for each event handler: / Event – Event that is processed, e.g. CLICKED. / Handler type – There are two options: Flow or Action. If Flow is selected, a flow output will be added through which the event is processed, and if Action is selected, then it is necessary to specify which User action will be performed during event processing. / Action - If the Handler type is set to Action, then here we need to enter the name of the User action that will be performed during the processing of the selected event.

Flow
### Inputs Array / Additional component inputs that the user can add as desired in order to use them to receive additional data needed when evaluating expressions in properties. Each input is given a name and type. Name is used when referencing an input within an expression. A type is used to project Check to check whether a data line that transmits data of that type is connected to the input or not. / ### Outputs Array / Additional component outputs that the user can add to send data through. Each output is assigned a name and type. An example of using this output is e.g. in the Loop component, where we can put the output name for the Variable property instead of e.g. variable name. In that case, the Loop component will not change the content of the variable in each step, but will send the current value through that output. / ### Catch error Boolean / If this checkbox is enabled then an @Error output will be added to the component and if an error occurs in this component during the execution of the Flow, the Flow will continue through that output. The data that will be passed through that output is the textual description of the error.

## Examples

- Line Chart
- EEZ Chart
- Rigol Waveform Data